## Slide 1: Air Hockey Robot Mechanical Design
Version 1
February 2, 2018
Thomas Abdallah

## Slide 2: Version 1 Design Goals
Prove out feasibility of belt-driven mechanism on an 1.8m x 0.9m Air Hockey Table
Enable a functional development platform early in the project
  Gain knowledge to inform future design decisions
    Mass of the moving X-Axis assembly
    Robustness of 3D printed components
    Encoder based position tracking accuracy
    Etc.

## Slide 3: Design Overview
Belt driven mechanism inspired by open-source project
  https://www.jjrobots.com/air-hockey-robot-a-3d-printer-hack/
  Redesigned to accommodate larger table, implemented numerous improvements to improve robustness & ease of manufacturing
3 motors (2 Y-Axis, 1 X-Axis)
  Easy to swap different motors later in the project
Utilizes off the shelf bearings, pulleys and belts
Mounting brackets 3D printed (own design)
Paddle 3D printed (open-source design)
Y
X

## Slide 4: Design Overview
Idler Pulley
Motor + GT2 Timing Pulley
Guide Rod + Belt
Carriage + Linear Bearing

## Slide 5: Design Overview

## Slide 6: Y-Axis Motor Assembly
Mount design controls position in 3 dimensions
  Bolt hole placement controls Y-Dimension
Motor selected for prototyping purposes
  May change later once system level design complete
  Includes integrated encoder
GT2 30-Tooth timing pulley drives belt
  May change later once system level design complete

## Slide 7: Y-Axis Idler Pulley Assembly
Mount design controls position in 3 dimensions
  Bolt hole placement controls Y-Dimension
Idler pulley mounted on 5x16 ball bearings allowing it to rotate freely

## Slide 8: X-Axis Motor + Idler Pulley Assemblies
Motor Assembly
Common carriage design
  Linear bearing allows smooth translation on y-axis guide rod
  Opening above belt track to allow for easy tensioning
Idler Pulley Assembly

## Slide 9: Paddle Assembly
Open-source design
Uses linear bearings to allow for smooth translation on x-axis guide rods
Opening in belt track to allow for easy belt tensioning